## Slide 1: 计组分享
2024.5.16
讲解人：马锦鹏 邵一均

## Slide 2
单周期处理器
关键路径问题
1
2
数据通路
3
控制信号问题

## Slide 3: Instructions
R-Type: add, sub, and, or, slt
Memory: lw, sw
Branch: beq, j
2
address
31:26
25:0
Jump
Notes: R-格式的指令执行涉及的数据通路
需要从寄存器堆中读取两个值，运算后写入到指定的寄存器中

## Slide 4: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result
Notes: R-格式的指令执行涉及的数据通路
需要从寄存器堆中读取两个值，运算后写入到指定的寄存器中

## Slide 5: R-Type Instruction
add rd, rs, rt
Notes: 有了基本的数据通路之后，需要测试这些数据通路是否正确。我们将分别测试3类指令是否能够在该数据通路上正确地被执行。
下面我们浅色部分的部件为不使用的部件。

## Slide 6: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory
Notes: 读取数据指令，执行时涉及的数据通路
读取寄存器操作数
与 16位的立即数运算的偏移地址运算读写的内存的地址

## Slide 7: Load Instruction
lw rt, offset(rs)
Notes: 对于Load指令或者Store指令
浅色部分的部件为不使用的部件。

## Slide 8: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch
Notes: 分支指令：
读取寄存器操作数
比较运算
计算目标地址

## Slide 9: Branch-on-Equal Instruction
beq rs, rt
Notes: 对于Branch指令
浅色部分的部件为不使用的部件。

## Slide 10: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 11: Datapath With Jumps Added
Notes: 浅色部分的部件为不使用的部件。

## Slide 12: Critical Path-Load
lw rt, offset(rs)
I-MEM + Regs + MUX + ALU + D-MEM + MUX + Regs
T(ADD) < T(I-MEM)
T(SIG-Extend) < T(Regs)

## Slide 13: Control Signals-Load
lw rt, offset(rs)
R型指令 aluop = 00
Lw,sw aluop = 01
Beq aluop = 10
0
1
1
1
1
0
0
1
0

## Slide 14: Critical Path-Branch
beq rs, rt
I-MEM + Regs + MUX + ALU + MUX
T(Shift-Left2) + T(ADD) < T(MUX) + T(ALU)
Notes: 对于Branch指令
浅色部分的部件为不使用的部件。

## Slide 15: Control Signals-Branch
beq rs, rt
R型指令 aluop = 00
Lw,sw aluop = 01
Beq aluop = 10
x
0
0
0
0
0
1
0
1
Notes: 对于Branch指令
浅色部分的部件为不使用的部件。

## Slide 16: Control Signals
Instruction | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 0 | X | X | X | 0 | X | XX | 1

## Slide 17
流水线处理器
1
数据通路
2
冲突问题

## Slide 18
Single-Cycle vs. Pipelined

## Slide 19
Single-Cycle & Pipelined Datapath

## Slide 20
WriteReg must arrive at same time as Result
Corrected Pipelined Datapath

## Slide 21
When an instruction depends on result from instruction that hasn’t completed
Types:
  Data hazard: register value not yet written back to register file (Read after Write)
  Control hazard: next instruction not decided yet (caused by branches)
Pipeline Hazards

## Slide 22
Data Hazard – R Type Write

## Slide 23
Data Forwarding (Bypassing)

## Slide 24
Data Forwarding

## Slide 25
Forward to Execute stage from either:
  Memory stage or
  Writeback stage
Forwarding logic for ForwardAE:
if ((rsE != 0) AND (rsE == WriteRegM) AND RegWriteM)
then ForwardAE = 10
else if ((rsE != 0) AND (rsE == WriteRegW) AND RegWriteW)
then ForwardAE = 01
else ForwardAE = 00
Forwarding logic for ForwardBE same, but replace rsE with rtE
Data Forwarding

## Slide 26
Data Hazard – Load Write

## Slide 27
Stalling – Load Write

## Slide 28
Stalling Hardware

## Slide 29
lwstall =
((rsD==rtE) OR (rtD==rtE)) AND MemtoRegE
StallF = StallD = FlushE = lwstall
Stalling Logic

## Slide 30
beq:
  branch not determined until 4th stage of pipeline
  Instructions after branch fetched before branch occurs
  These instructions must be flushed if branch happens
Branch misprediction penalty
  number of instruction flushed when branch is taken
  May be reduced by determining branch earlier
Control Hazards

## Slide 31
Control Hazards

## Slide 32
Early Branch Resolution

## Slide 33
Introduced another data hazard in Decode stage
Early Branch Resolution

## Slide 34
Stalling – R Type Write
add t0, s1, s2
beq t0, t1

## Slide 35
Data Hazard – R Type Write
add t0, s1, s2
nop
beq t0, t1

## Slide 36
Stalling – Load Write
lw t1, offset(s3)
beq t0, t1
lw t1, offset(s3)
nop
nop
beq t0, t1

## Slide 37
Forwarding logic:
ForwardAD = (rsD !=0) AND (rsD == WriteRegM) AND RegWriteM
ForwardBD = (rtD !=0) AND (rtD == WriteRegM) AND RegWriteM
Stalling logic:
branchstall = BranchD AND RegWriteE AND
(WriteRegE == rsD OR WriteRegE == rtD)
OR
BranchD AND MemtoRegM AND
(WriteRegM == rsD OR WriteRegM == rtD)
StallF = StallD = FlushE = lwstall OR branchstall
Control Forwarding & Stalling Logic